Adept Arm, Atlas Hand Moving Guide:
1. Start roscore
2. Make sure the flor_repo is sourced in .bashrc
3. Start convex hull:
  Start new terminal, “rosrun hullify hull_tests”
  Start new terminal, “rosrun hullify convex_hull” Avoid entering configuration until MoveIt is running
4. Start new terminal, “sudo minicom”
  Follow instructions in ROS Setup Instructions, osu_ros_adept/docs
5. Start new terminal, “sudo -s”
  “source catkin_ws_v2/install/setup.bash”
  “rosrun osu_ros_adept controller_comm_client.py” It should say “Spinning” when started. This means connection to robot is established.
6. Start new terminal, “source catkin_ws_v2/install/setup.bash”
  “roslaunch adept_moveit_generated2 demo.launch”
  In step 3 terminal:
  When the robot is in simulation, go to Rviz and find the fixed frame of the scene. Put this into the convex hull program configuration (e.g. fixed_frame: “adept_arm” → config: “/adept_arm”). Further, use /testing/default as the pointcloud input and /hull_mesh as the base name.
7. Start new terminal, “source catkin_ws_v2/devel/setup.bash”
  “rosrun moveit_int programmatic_moveit”
8. Go the hull_tests terminal (step 3 again) and begin entering portions of spheres. The density number is between 1 and 0 and determines how many points will be on the hull. The terminal angle entry is in radians and describes when the dome ends.